WG « Revision C37.011 :  IEEE Application Guide for TRV for AC High-Voltage Circuit Breakers »

A revision is under way to align the text with the new TRV requirements introduced in ANSI/IEEE C37.04, ANSI C37.06 and ANSI C37.06.1.

Specifically, this revision is necessary for two reasons :

the TRV requirements have changed in the latest editions of ANSI/IEEE C37.04, ANSI C37.06 and are further changing to harmonize with IEC 62271-100,

the part on TRV associated with transformer limited faults must be aligned with ANSI Std C37.06.1.

Major changes implemented in this guide:

the TRV capability of circuit breakers is described by 2 or 4 parameters,

a new annex gives explanations and guidance on the selection of the first pole to clear factor,

additional explanations are given to justify the parameters used for short-line fault testing (surge impedance, peak factor).

The present IEEE Std C37.011-1004 has been extended until the expiration of the PAR for PC37.011 (October 2005).

Denis Dufournet

Chair WG Revision C37.011